## Slide 1
Microwave Signal Loss Prediction
One-Step Ahead Forecasting with Multiple Linear Regression (MLR)
Prepared by: Cem Sondur
Data: Hourly Simulation | Duration: 1 Year (8760 hours) | Features: 5 | Language: R
Machine Learning Project

## Slide 2
Project Flow
1
Data Generation
8760-hour ARIMA-based simulation: Rain, Temperature, Wind, and a realistic signal loss model
2
Feature Engineering
Lag features: Loss_Lag1 and Rain_Lag1 → time series structure for one-step ahead prediction
3
Model Setup
MLR: lm() function, 5 independent variables, 80%/20% train/test split
4
Model Validation
Visual validation with 5 plots: Actual vs Predicted, Residual analysis, Q-Q, Time, Coefficients
5
Performance Metrics
R²=72.83%, MAE=0.2947 dB, RMSE=0.3695 dB, MAPE=1.41% → Operational success

## Slide 3
Theoretical Background: Multiple Linear Regression (MLR)
ŷ = β₀ + β₁·Rain + β₂·Temp + β₃·Wind + β₄·Rain_Lag1 + β₅·Loss_Lag1 + ε
What Are the β Coefficients?
β₀: Constant term (intercept) — the expected loss value when all variables equal 0
β₁...β₅: The independent effect of each feature — how many dB the loss changes for a 1-unit increase while other variables are held constant
With the OLS (Ordinary Least Squares) method, β values are estimated so as to minimize the sum of squared residuals
One-Step Ahead Forecasting
Goal: Predict the Next_Loss value at time t+1 using information available at time t
Loss_Lag1 = Loss(t-1), Rain_Lag1 = Rain(t-1) → carries past information into the model
This structure turns classic MLR into a time series forecaster — the past instant is used to predict the future instant
MLR Assumptions
Linearity: There is a linear relationship between the dependent and independent variables
Normality: Residuals (ε) should be normally distributed → tested with Q-Q plot
Homoscedasticity: Variance of residuals should be constant → verified with Residuals over time

## Slide 4
Dataset: Simulation Design and Physical Model
Feature
Generation Method
Unit / Range
Rain
ARIMA(ar=0.98) × season
mm/h, ≥0
Temp
Sine (annual+daily) + noise
°C, ~17–33
Wind
ARIMA(ar=0.95) + constant
m/s, ≥0
Loss_Lag1
Previous hour's Loss value
dB
Rain_Lag1
Previous hour's Rain value
mm/h
# Signal loss physical model (ITU-R based)
signal_loss <- 20 +
(0.00454*(rain^1.353)*10) +
(0.0003*temp) + (0.05*wind)
+ rnorm(N, 0, 0.3)
Why the ITU-R formula?
The International Telecommunication Union's rain attenuation model — the rain^1.353 exponential effect represents real physical behavior.
Data Splitting Strategy
TRAIN 80% → 7007 hours
TEST 20% → 1751 hours
Chronological order preserved — no random shuffling (time series integrity)

## Slide 5
R Code — Step 1: Data Generation
set.seed(42) # Reproducibility N <- 8760 # 365 days × 24 hours # Rain: autocorrelated + seasonal rain_rate <- abs(arima.sim(list(ar=0.98), n=N))*2 *
(
1 + 0.4*sin(2*pi*day_of_year/365 - pi/2)) # Temperature: annual + daily sine + noise temp <- 25 + 8*sin(...) + 2*sin(...) + rnorm(N,0,0.5) # Signal loss (ITU-R model) signal_loss <- 20 +
(
0.00454*(rain_rate^1.353)*10) +
(
0.0003*temp) + (0.05*wind) +
rnorm(N,
0, 0.3) # ±0.3 dB measurement noise
set.seed(42)
Fixes the random number generator. The same data is produced on every run — results are reproducible.
arima.sim(ar=0.98)
AR coefficient 0.98 → rain shows 'persistence'. Mimics the autocorrelation in real weather data.
sin(2π × day/365)
Annual seasonality: low rain in winter, high in summer. Temperature is modeled with a sine wave in the same way.
rain^1.353 exponential effect
ITU-R P.838 standard. As rain intensity rises, signal loss increases exponentially, not linearly.
rnorm(N, 0, 0.3)
±0.3 dB measurement noise added. Represents sensor uncertainty in real systems.

## Slide 6
R Code — Steps 2 & 3: Model Setup and Metric Computation
# Lag features (one-step ahead) mw_data$Loss_Lag1 <- c(NA, mw_data$Loss[-N]) mw_data$Rain_Lag1 <- c(NA, mw_data$Rain[-N]) mw_data$Next_Loss <- c(mw_data$Loss[-1], NA) mw_data <- na.omit(mw_data) # Train / Test split (80%-20%) split_idx <- floor(0.8 * nrow(mw_data)) train_data <- mw_data[1:split_idx, ] test_data <- mw_data[(split_idx+1):nrow(mw_data), ] # MLR model — 5 features model <- lm(Next_Loss ~ Rain + Temp + Wind + Rain_Lag1 + Loss_Lag1, data = train_data) # Error metrics Residuals <- Predicted - Actual R2 <- 1 - sum(Residuals^2) / sum((Actual - mean(Actual))^2) MAE <- mean(abs(Residuals)) MAPE <- mean(abs(Residuals / Actual)) * 100
c(NA, Loss[-N])
Shifts the vector one step to the left. Writes the value at time t into row t-1 → lag feature.
Next_Loss target
c(Loss[-1], NA): a one-step forward shift. Stores t+1's loss as the target in the row at time t.
na.omit()
Loss_Lag1=NA in the first row, Next_Loss=NA in the last. Removes these two rows from the dataset.
lm() function
R's core OLS (Ordinary Least Squares) regression function. Computes coefficients analytically — no iteration needed.
R² formula
1 − (SS_res / SS_tot). Close to 1 means the model explains variance well; close to 0 means it's no better than the mean.

## Slide 7
Plot 1: Actual vs Predicted Loss
45° Reference Line
The red dashed line marks a perfect prediction. Points above this line mean the model is underestimating.
Tight Point Band
Predictions cluster within ±0.5 dB of the actual values. Low scatter → the model is consistent.
Underestimation (23–24 dB)
During heavy rain spikes the model lags behind. Because Loss_Lag1 uses the previous instant, it cannot capture sudden changes.
Overall Comment
The linear relationship is strong and monotonic. R²=72.83% is fully consistent with this visual distribution.

## Slide 8
Plots 2 & 3: Residual Distribution and Normality Test (Q-Q)
Histogram Interpretation
Residuals are centered around 0 with a bell-curve-like shape. There is slight right skew (positive rain spikes). MLR's normality assumption is largely met. The red line shows the median is close to 0.
Q-Q Plot Interpretation
Points hug the reference line almost perfectly → residuals are normally distributed. In the left tail (around −3) 4–5 points fall below the line: a slight heavy-tail in extreme negative residuals. Conclusion: the normality assumption is VALID.

## Slide 9
Plot 4: Residuals Over Time — MLR Assumption Check
✅ Around Zero
Residuals fluctuate around the 0 line with no systematic direction. The model is unbiased.
✅ Homoscedasticity
Variance is constant over time. Start and end have similar spread → MLR assumption satisfied.
✅ No Autocorrelation
No clear periodic pattern is visible. Residuals are independent → the model isn't missing any structural feature.
⚠️ ±1 dB Overshoot Points
Errors grow on sudden rain spikes. Due to the lag structure, the model can fall behind.
This plot visually confirms MLR's 3 core assumptions (normality, independence, constant variance).

## Slide 10
Plot 5: Feature Coefficients and Multicollinearity Analysis
1. Loss_Lag1 → β ≈ +0.17 (Dominant)
Signal loss changes very slowly. The loss one hour earlier is the strongest predictor of the current loss. Principle of physical continuity.
2. Rain → β ≈ +0.13 (Second Most Important)
Instantaneous rain directly affects the microwave signal. Because the data was generated via the ITU-R model, the coefficient is significant and positive.
⚠️ Rain_Lag1 → Negative Coefficient — Why?
Multicollinearity: Rain and Rain_Lag1 are highly correlated (r≈0.98). OLS "goes astray" when distributing coefficients. Information Overlap: Loss_Lag1 already contains the effect of past rain. To avoid double-counting, the model balances by pulling Rain_Lag1 negative.

## Slide 11
Performance Metrics
R²
72.83%
Explained Variance
Explains ~¾ of the variability
MAE
0.2947 dB
Mean Absolute Error
Mean error < 0.3 dB
RMSE
0.3695 dB
Root Mean Squared Error
Close to MAE → few outliers
MAPE
1.41%
Mean Absolute Percentage Error
Strongest metric — excellent
Metric Formulas and Interpretations
MAE = (1/n)Σ|yᵢ−ŷᵢ| → Mean absolute error; treats large and small errors with equal weight. RMSE = √[(1/n)Σ(yᵢ−ŷᵢ)²] → Penalizes large errors more heavily. RMSE≈MAE implies no significant outliers. MAPE = (100/n)Σ|yᵢ−ŷᵢ|/|yᵢ| → Percentage error; a value of 1.41% is considered operationally excellent.

## Slide 12
Overall Summary
Project Summary — What Did We Do?
Problem
Predicting hourly microwave signal loss 1 hour ahead
Method
Multiple Linear Regression (MLR) — lm() — with OLS
Data
8760-hour simulation; ARIMA-based rain, sinusoidal temperature, ITU-R loss model
Features
Rain, Temp, Wind + time series lags: Rain_Lag1, Loss_Lag1 (5 total)
Train/Test
80% chronological training (7007 hours) / 20% test (1751 hours)
Findings
R²=72.83%, MAE=0.29 dB, RMSE=0.37 dB, MAPE=1.41% — Operational success
Model Strength
Loss_Lag1 is the dominant feature; Rain, Wind, and Temp provide meaningful contribution
Key Finding
Rain_Lag1 has a negative coefficient: multicollinearity + information overlap detected
MLR Assumption Check
✅ Normality
Q-Q Plot — satisfied
✅ Homoscedasticity
Residuals over time — satisfied
✅ Independence
Time plot — satisfied
⚠️ Multicollinearity
Rain / Rain_Lag1 — detected
Limitations and Improvement Suggestions
• Simulated data: Results may differ with real measurement data • Multicollinearity: Can be quantified numerically with VIF analysis • Better model: R² could be improved with ARIMA, Random Forest, or LSTM • R² = 72%: Natural ceiling imposed by stochastic rain noise

## Slide 13
Thank You
Cem Sondur
Machine Learning Project • Microwave Signal Loss Prediction with MLR
R²
72.83%
MAE
0.29 dB
RMSE
0.37 dB
MAPE
1.41%
I'm ready for your questions.